## Slide 1: LOINC and NPU
The LOINC system allows different units for each measurand.
In the NPU system the measurement units, for results expressed by numbers and units, are precoordinated for each measurand.
The two terminologies based on similar principles. Measurands are described by three major axes; system, component, and kind-of-property.

## Slide 2: Differences in the understanding of the term ”System”
NPU understands System as the metrological system:
Example 1: For glucose concentration in blood plasma, measured in full blood, e.g. by a blood gas device, the NPU System is Plasma.
NPU02192 P—Glucose; subst.c. = ? mmol/L
Example 2: For the number fraction of lymphocytes in a differential count of leukocytes, the NPU System is Leukocytes, as the denominator in the fraction of lymphocytes.
NPU03965 Lkcs(B)—Lymphocytes; num.fr. = ?
LOINC understands System as the specimen type:
Example 1: For glucose concentration in blood plasma, measured in full blood by a blood gas device, the LOINC System is Blood
15074-8 Glucose [Moles/volume] in Blood
Example 2: For the number fraction of lymphocytes in a differential count of leukocytes, the LOINC System is Blood,
26478-8 Lymphocytes/100 leukocytes in Blood
The ”Litre” in the unit refers to volume of the system
Not clear what ”volume” refers to?

## Slide 3: Differences in spelling for some component terms
LOINC term |  | NPU term | Comment
Basophils |  | Basophilocytes | Unconventional NPU spelling
Creatinine |  | Creatininium | Unconventional NPU spelling
Eosinophils |  | Eosinophilocyte | Unconventional NPU spelling
C reactive protein |  | C-reactive protein | Random spelling differences
pH |  | Hydrogen ion | Random spelling differences
Bilirubin |  | Bilirubins | Random spelling differences
Hemoglobin |  | Haemoglobin | American versus European language
Epinephrine |  | Adrenalinium | American versus European language
Norepineprine |  | Noradrenalinium | American versus European language
glyBURIDE |  | Glibenclamide | American versus European language
Albuterol |  | Salbutamol | American versus European language

## Slide 4: Differences in the principles for naming components
In the LOINC terminology the Component is often the name of the analyte, but in some cases it is a name of the procedure.
Example: Eosin-5-Maleimide binding [Presence] in Blood by Flow cytometry (FC)
In the NPU terminology the Component is always the name of the analyte of the intended measurand
Example:
Ercs(B)—Band 3 anion transport protein; rel.entitic num

## Slide 5: Differences in the understanding of the concept ”kind-of-property”
Entitic Mass <LOINC>
entitic mass <NPU>
Mass Concentraton <LOINC>
mass concentration <NPU>
Most of 150 different kind-of-properties have identical meanings. Examples:
arbitrary concentration<NPU>
Precence or Threshold<LOINC>
arbitrary entitic number<NPU>
Arbitrary Concentration<LOINC>
arbitrary substance concentration <NPU>
Dilution factor<LOINC>
Some kind-of-properties have broader or smaller meanings. Examples:

## Slide 6: Differences in specification of methods
LOINC: Examination techniques precoordinated to to indicate the quality of the measurement:
Example of various ”method types”:
  GC
  Glucometer
  High sensitive
  IA
  IA rapid
  ISE
  LA
  LC/MS/MS
  Nephelometry
  PEG assay
NPU: Examination principles are included in the codes when needed to define what is measured.
Example of method principles for measurement of fibrinogen:
  immunoassay
  coagulation
  thrombelstography

## Slide 7: Differences in specification of standards
NPU: For results presented with International Units (IU) are the definition of the unit included as a specification in the code.
NPU02482 P—Immunoglobulin E; arb.subst.c.(IRP 75/502; proc.) = ? × 10³ IU/L
NPU18868 P—Immunoglobulin E; arb.subst.c.(WHO 68/341; proc.) = ? × 10³ IU/L
NPU56406 P—Immunoglobulin E; arb.subst.c.(IS 11/234; proc.) = ? × 10³ IU/L
LOINC: Information about standards are normally not precoordinated
19113-0 IgE [Units/volume] in Serum or Plasma

## Slide 8: Summary: half of the common measurands can be mapped by logical rules and string mapping of terms

## Slide 9: What is the Component when coulor is the Kind-of-property?
NPU code | Short definition
NPU17026 | Csf—Cerebrospinal fluid; colour(proc.) = ?
NPU18210 | Asc—Ascitic fluid; colour(proc.) = ?
NPU18214 | Plf(spec.)—Pleural fluid; colour(proc.) = ?
NPU20195 | U—Urine; colour(proc.) = ?
NPU21728 | Csf—Cerebrospinal fluid; colour(before spinn.; proc.) = ?
NPU54861 | Asc—Ascitic fluid; colour(before spinn.; proc.) = ?
In the NPU terminology are System and Component for physical properties of these kinds often identical (like a set with only one element).
Some examples:

## Slide 10
gunnar.nordin@equalis.se